## Slide 1
Run a cocotb example
Browser sketches taught async tests, triggers, DUT handles, BinaryValue, scoreboards, and wave literacy
learn_cocotb — offline cocotb example
Notes: Browser sketches taught async tests, triggers, DUT handles, BinaryValue, scoreboards, and wave literacy. This module is Track A only: you open a real cocotb example with a simulator such as Verilator and run it on your machine. You leave with a command line you can repeat—activate the environment, make, run, and read pass or fail. No browser lab required here—just the live toolchain.

## Slide 2
Why leave the browser
Sketches are concept literacy, they do not compile a DUT or exercise cocotb Makefiles
The glue you will keep at work
The monorepo links the legacy learn-uvm-pyuvm tree for a small and-gate cocotb test you
One clean pass is enough for this module
learn_cocotb — offline cocotb example
Notes: Sketches are concept literacy—they do not compile a DUT or exercise cocotb Makefiles. Offline runs force you through Python packages, simulator flags, MODULE and TOPLEVEL wiring, and the glue you will keep at work. The monorepo links the legacy learn-uvm-pyuvm tree for a small and-gate cocotb test you can run today. One clean pass is enough for this module; you can deepen pyuvm tests later on the next course.

## Slide 3
Offline workflow
Here is the rhythm
Open the legacy course next to this curriculum
Activate its virtual environment so cocotb is on your path
Change into the module-one cocotb tests folder
Run make with Verilator as the simulator and the and-gate test selected
Watch compile finish, then the cocotb runner start
learn_cocotb — offline cocotb example
Notes: Here is the rhythm. Open the legacy course next to this curriculum. Activate its virtual environment so cocotb is on your path. Change into the module-one cocotb tests folder. Run make with Verilator as the simulator and the and-gate test selected. Watch compile finish, then the cocotb runner start. Capture the command and the pass or fail line in your notes. Other simulators swap the SIM knob—same idea, different Make recipe.

## Slide 4
Real cocotb track practice
In the real cocotb track
Activate the virtual environment
List the cocotb tests directory; you should see the Makefile and the and-gate test file
Then change into that folder and run make
SIM selects the simulator, here Verilator
Say the working directory aloud before make so you know where the build runs from
learn_cocotb — offline cocotb example
Notes: In the real cocotb track, change into the legacy offline course tree so your shell sits where the examples live. Activate the virtual environment—or prepend its bin folder to your path—so cocotb resolves. List the cocotb tests directory; you should see the Makefile and the and-gate test file. Then change into that folder and run make. SIM selects the simulator—here Verilator—and TEST names which cocotb module to run—here the and-gate test. Say the working directory aloud before make so you know where the build runs from.

## Slide 5
Real cocotb track practice — try these
# cd learn_uvm_pyuvm — enter the legacy offline course
cd courses/learn_uvm_pyuvm
# source .venv/bin/activate — put cocotb on PATH
source .venv/bin/activate
# ls module1/tests/cocotb_tests — find Makefile and test_and_gate.py
ls module1/tests/cocotb_tests
# make SIM=verilator TEST=test_and_gate — compile and run
cd module1/tests/cocotb_tests
make SIM=verilator TEST=test_and_gate
learn_cocotb — offline cocotb example

## Slide 6
Pitfalls to watch
Without the virtual environment
Make must run from the test folder that owns the Makefile
A browser sketch pass is not a simulator pass, offline needs a real binary
The first Verilator plus cocotb compile can take a minute
If Verilator is missing, install it or swap SIM to a simulator your site supports
learn_cocotb — offline cocotb example
Notes: Without the virtual environment, system Python may lack cocotb—activate first, or fix PATH. Make must run from the test folder that owns the Makefile; the wrong directory fails quietly or builds nothing useful. A browser sketch pass is not a simulator pass—offline needs a real binary. The first Verilator plus cocotb compile can take a minute; later rebuilds are faster when objects exist. If Verilator is missing, install it or swap SIM to a simulator your site supports.

## Slide 7
Your turn
Complete the offline checklist
Prefer module-one and-gate unless your site policy points elsewhere
When you are ready
learn_cocotb — offline cocotb example
Notes: Complete the offline checklist: locate a runnable example, build it, observe pass or fail, and note your simulator and package versions. Prefer module-one and-gate unless your site policy points elsewhere. When you are ready, take the short quiz, then continue to the wrap module that closes this cocotb path.